## Slide 1
F-17 Humanitarian Hummingbird
SPECIFIC DYNAMICS
Chloe Fulbrook Ethan Sam Khai Huynh Vikram Procter Caleb Garcia Minh Do
HOOD RESEARCH
DEPARTMENT
January-April 2026
Problem Statement
Flight Controls
Communications
No sub-250g, modular, affordable microdrone exists on the market. Addresses that gap through an adaptable platform for surveying and UAV applications.
Testing & Results
Wirelessly communicated flight controls drive a PID loop utilizing a Mahony filter to achieve flight
Centered around a STM32f4 running bare-metal C firmware to control four brushless DC motors via 12 half bridges.
ENEL 400 | Electrical Engineering - Schulich School of Engineering
Sensorless interrupt driven trapezoidal six-step commutation allows for efficiencies over 50% better than off-the-shelf alternatives.
The controller relays two bi-axial gimbal controls, four buttons, and one arming switch to the flight control board via ESP-NOW. Implements fault disable
safety logic and
allows a range of
over 20m.
7 custom PCBs. Over 3000 lines of code. Achieves stable control for ~5min flight times. Set up for modular development and autonomous control expansions.
attitude targets. Specifies motor speeds using 50Hz PWM to ESCs.
Mechanical Design
Thrust to weight ratio up to 2.32 and light weight construction means incredible maneuverability.
Brushless DC Motor Driver